## Slide 1
a discrete-event simulation study
The FermaCore Tablet Line
Where is the bottleneck — and can the line meet 2030 demand within its existing capacity?
Jacob Brams (s224927)
Group 16 · Manufacturing · 42417 Simulation in Operations Management · June 2026
Jacob Brams · s224927 · 42417 FermaCore
Notes: === SLIDE 1 — TITLE === [target 0:00–0:25] Hi, my name is Jacob Brams. [pause] This is our discrete-event simulation of the FermaCore tablet production line, which we built in AnyLogic. FermaCore is a pharmaceutical line that mixes batch-type operations up front with rate-based packaging at the end. [pause] The reason this matters: management's 2030 plan wants to raise output — but they want to do it within the equipment they already have, before committing to anything with a long lead time. So this study answers two questions. First: where is the bottleneck on the line today? And second: can the line absorb rising 2030 demand without new capacity? [breathe] I'll take you through the findings. [ADVANCE to slide 2]

## Slide 2
performance management
Five S.M.A.R.T. KPIs anchor the whole study
60,494
bottles / run
(throughput)
94.3%
dryer utilisation
(bottleneck)
179 h
mean flow time
98%
on-time delivery
6.2%
scrap rate
(yield)
Four primary KPIs cover output, the binding constraint, congestion and schedule adherence; one secondary KPI covers material efficiency. Every metric is measured directly from the model each run, so improvement scenarios are compared on the same footing.
These are the baseline values — the reference the rest of the study moves against.
Jacob Brams · s224927 · 42417 FermaCore
Notes: === SLIDE 2 — KPIs / BASELINE === [target 0:25–0:55] To judge the line and compare improvements, we track five KPIs, and we framed each one using the SMART criteria. [pause] Four are primary. Throughput, in bottles, is the output. Station utilisation tells us which resource is the binding constraint. Flow time and WIP measure congestion. And on-time delivery measures schedule adherence. The fifth — yield — is a secondary efficiency metric. [breathe] The numbers on screen are the baseline values. Just over sixty thousand bottles per run. The dryer running hottest, at ninety-four point three percent. Mean flow time of a hundred and seventy-nine hours. Ninety-eight percent on time. And six point two percent scrap. [pause] I want you to hold onto that dryer number — ninety-four percent — because it turns out to be the headline of the entire study. Everything that follows is measured against this baseline. [ADVANCE to slide 3]

## Slide 3
experimental study
No capacity lever moves throughput
2³ factorial effects on weekly throughput (bottles) — none is significant
Chart: 
| C: packaging | AC | AB | A: dryer | B: clean | BC | ABC
Effect | 454 | -277 | -253 | -166 | 158 | -131 | -32
Why?
Output is fixed by batches × per-batch yield, not by station capacity.
Largest effect is +454 bottles at t = 1.31 — inside the noise band. A single-lever (OFAT) test would have hidden this.
Jacob Brams · s224927 · 42417 FermaCore
Notes: === SLIDE 5 — EXPERIMENTAL STUDY / DOE === [target 2:05–2:40] Now to the experiments. We first screened the levers, then ran a full two-cubed factorial design on the three capacity stations — dryer, cleaning team, and packaging. [pause] We deliberately used a full factorial rather than testing one factor at a time, so that interaction effects between the levers are actually visible. [breathe] And here's the result — the chart on the left. Not a single effect is statistically significant. The largest is a packaging effect of plus four hundred and fifty-four bottles, but that sits at a t-value of just one point three one, well inside the noise band. [pause] The reason is structural, and it's the central insight of the whole study. At a fixed fifty-batch plan, output is set by the number of batches times the per-batch yield — not by how much machine capacity you add. So adding capacity simply cannot raise output here. [pause] And notice: a one-factor-at-a-time test would have missed this completely — it might even have misread random scatter between two runs as a real improvement. [ADVANCE to slide 6]

## Slide 4
bottleneck shift
Adding a dryer just relocates the constraint
Chart: 
| Baseline | +1 dryer | +dryer +clean | Best combo
Dryer | 94.3 | 78.5 | 61.1 | 78.2
Cleaning team | 79.6 | 95 | 93 | 92.8
Packaging | 52.4 | 72.2 | 93 | 76.7
The pattern
Drying binds at 94%. A 2nd dryer drops it to 79% - but its 2-hour clean shoves the shared cleaning team to 95%.
Throughput never follows — it holds at approx. 60,500.
Jacob Brams · s224927 · 42417 FermaCore
Notes: === SLIDE 6 — BOTTLENECK SHIFT === [target 2:40–3:15] This chart shows where the constraint actually sits as we add capacity. [pause] At baseline, on the far left, the dryer is the tall bar — ninety-four percent. Now add one dryer. Drying drops to seventy-nine percent — relieved. But watch the orange bar: the cleaning team jumps up to ninety-five percent. [breathe] Why? Because each dryer carries a two-hour clean, and all the cleaning is done by one shared cleaning team. So relieving the dryer just loads up the team. Add a cleaning-team member as well, and the load simply spreads onto packaging instead. [pause] The constraint keeps moving — but throughput never follows. It stays right around sixty thousand five hundred bottles in every single configuration. [pause] That coupling between the dryer and the shared cleaning team is a structural limit. It's something you relocate by adding machines — but you don't remove it that way. [ADVANCE to slide 7]

## Slide 5
2030 demand sweep
Output scales — but service collapses
Chart: On-time delivery vs order-book size
| 50 (today) | 75 | 100
On-time delivery (%) | 100 | 71 | 54
As the order book grows (batches →)
Bottles shipped
60,494 → 123,496
Dryer utilisation
94.3% → 96.8%
Mean flow time
179 h → 338 h
On-time delivery
100% → 54%
The line PRODUCES the volume — but lead time doubles and on-time delivery falls to 54%. The single dryer saturates.
Jacob Brams · s224927 · 42417 FermaCore
7 / 8
Notes: === SLIDE 7 — 2030 DEMAND SWEEP === [target 3:15–3:50] So that's today's order book. The 2030 question is about volume. We grew the order book itself — from fifty batches, to seventy-five, to a hundred — holding the product mix fixed, so only the volume changes. [pause] First, the good news. The line does produce the extra volume. Bottles shipped roughly double — from sixty thousand up to a hundred and twenty-three thousand. [breathe] Now the bad news, and it's the red line on the chart. As volume rises, the single dryer saturates. Mean flow time roughly doubles — from a hundred and seventy-nine hours to three hundred and thirty-eight. And on-time delivery collapses — from a hundred percent, down to seventy-one, and then to just fifty-four percent. [pause] And here's the hard part: adding capacity barely helps, because of that same dryer-and-clean coupling we just saw. [pause] So at current capacity, the line can only meet 2030 demand by letting its service fall apart. The real fix isn't another machine — it's decoupling the dryer clean from the shared team. [ADVANCE to slide 8]

## Slide 6
the decisive lever
Industry 4.0 is the only lever that lifts output
+8.0%
+4,842 bottles / run
95% CI [3,543, 6,141]
Predictive maintenance at the press: sensors catch force / fill-depth drift before it scraps tablets, cutting press scrap from 10% to 4%.
Because output is bounded by yield, raising good tablets per batch is the ONE thing that raises shipped output — and it needs only a sensor retrofit, no added line capacity.
Recommendation
1. Today: defer the line capital expansion  invest in the press-sensor scrap reduction.
2. Before 2030: decouple the dryer clean from the shared team  a second dryer alone only moves the bottleneck.
Jacob Brams · s224927 · 42417 FermaCore · 8 / 8
Notes: === SLIDE 8 — INDUSTRY 4.0 + RECOMMENDATION === [target 3:50–4:30] So if capacity doesn't raise output — what does? [pause] One thing, and one thing only: Industry four point zero. Predictive maintenance at the tablet press. Sensors monitor press force and fill depth and catch the drift before it scraps tablets — so a developing fault gets corrected before it ruins material, instead of after. [breathe] That cuts press scrap from ten percent down to four. And because output is bounded by yield, raising good tablets per batch is the one intervention that lifts shipped output. A significant plus eight percent — almost five thousand more bottles per run — and it needs only a sensor retrofit. No new line, no long lead time. [pause] So our recommendation is twofold. [pause] Today: defer the capital expansion, and invest in the press-sensor scrap reduction. It's the only lever that pays off right now, at a fraction of the cost. And before 2030 volume actually arrives: address the dryer-and-clean coupling directly — because simply buying another dryer just moves the bottleneck onto the cleaning team. [pause] Thank you. [END — total ~4:30, leaves ~30s buffer for the live AnyLogic demo]